## Slide 1: COMP417 Introduction to Robotics and Intelligent Systems Lecture 13: Particle Filters

## Slide 2: bel(x): when a single Gaussian fails
The robot below has a noisy door sensor
  Not a microphone that tells if the door squeaks…

## Slide 3: bel(x): when a single Gaussian fails
The robot below has a noisy door sensor
  Not a microphone that tells if the door squeaks… rather a camera that says “I’m in front of a door”, but sometimes gets it wrong….

## Slide 4: bel(x): when a single Gaussian fails
The robot below has a noisy door sensor
  Not a microphone that tells if the door squeaks… rather a camera that says “I’m in front of a door”, but sometimes gets it wrong….
Suppose this robot “wakes up” and has the door sensor read 1:
  That means, we’d like our belief to be high everywhere a door exists, and lower everywhere else

## Slide 5: bel(x): when a single Gaussian fails
The robot below has a noisy door sensor
  Not a microphone that tells if the door squeaks… rather a camera that says “I’m in front of a door”, but sometimes gets it wrong….
Suppose this robot “wakes up” and has the door sensor read 1:
  That means, we’d like our belief to be high everywhere a door exists, and lower everywhere else
  Sometime like:

## Slide 6: Today 2 different ideas that can track this kind of “multi-modal” belief:
The histogram filter:
  Simple and impractical, but good to get the idea
The particle filter:
  Another “winning” algorithm in robotics, and competitor to the KF
  Widely used and important to know: luckily a bit lighter on math

## Slide 7: Discrete (aka Histogram) Filter
Store a vector of N numbers, where world is split into bins of size W/N
The value in each bin stores , with limited precision
Bayes filter math becomes loops over the bins

## Slide 8: Discrete Filter
Algorithm Discrete_Bayes_filter( Bel(x),d ):
h=0
If d is a perceptual data item z then
For all x do
For all x do
Else if d is an action data item u then
For all x do
Return Bel’(x)

## Slide 9: What is the complexity?
Stare at the “loop over all x”:
  Inside this, we compute an update which draws from all other x…

## Slide 10: What is the complexity?
Stare at the “loop over all x”:
  Inside this, we compute an update which draws from all other x…
Discrete histogram filter is quadratic or worse in the number of states
The number of states needed to uniformly grid an d-dimensional space grows exponentially with d
We almost never use this in practice. But the idea of computing based on discrete locations can be extended!

## Slide 11: Recommended reading
Lesson 3 in https://www.udacity.com/course/artificial-intelligence-for-robotics--cs373
Chapters 4.3 and 8.3 in the Probabilistic Robotics textbook

## Slide 12: KF vs EKF vs PF
 | Kalman Filter | Extended Kalman Filter | Particle Filter
Dynamics model | Linear | Nonlinear | Nonlinear
Sensor model | Linear | Nonlinear | Nonlinear
Noise | Gaussian (Unimodal) | Gaussian (Unimodal) | Multimodal
One peak
Multiple peaks

## Slide 13: How can we represent multimodal distributions?
https://www.opsclarity.com
Idea #1: Histograms
Advantages: the higher the number of bars the better the approximation is
Disadvantages: exponential dependence on number of dimensions
Note: this approach is called the Histogram Filter. It is useful for low-dimensional systems but we will not study it in this class.

## Slide 14: How can we represent multimodal distributions?
https://www.opsclarity.com
Idea #1: Histograms
Advantages: the higher the number of bars the better the approximation is
Disadvantages: exponential dependence on number of dimensions
Note: this approach is called the Histogram Filter. It is useful for low-dimensional systems but we will not study it in this class.
Idea #2: Function Approximation / Fitting
Unclear how to do Bayes’ filter updates and predictions in this case.

## Slide 15: How can we represent multimodal distributions?
https://www.opsclarity.com
Idea #1: Histograms
Advantages: the higher the number of bars the better the approximation is
Disadvantages: exponential dependence on number of dimensions
Note: this approach is called the Histogram Filter. It is useful for low-dimensional systems but we will not study it in this class.
Idea #2: Function Approximation
Unclear how to do Bayes’ filter updates and predictions in this case.
Idea #3: Weighted Particles
Advantages: easy to predict/update by treating each particle as a separate hypothesis whose weight is updated.
Disadvantages: need enough particles to “cover” the distribution

## Slide 16: How can we represent multimodal distributions?
https://www.opsclarity.com
Idea #1: Histograms
Advantages: the higher the number of bars the better the approximation is
Disadvantages: exponential dependence on number of dimensions
Note: this approach is called the Histogram Filter. It is useful for low-dimensional systems but we will not study it in this class.
Idea #2: Function Approximation
Unclear how to do Bayes’ filter updates and predictions in this case.
Idea #3: Weighted Particles
Advantages: easy to predict/update by treating each particle as a separate hypothesis whose weight is updated.
Disadvantages: need enough particles to “cover” the distribution
Higher density of
particles means
higher probability
mass
W = sum of all particles’ weights

## Slide 17: How can we represent multimodal distributions?
https://www.opsclarity.com
Idea #1: Histograms
Advantages: the higher the number of bars the better the approximation is
Disadvantages: exponential dependence on number of dimensions
Note: this approach is called the Histogram Filter. It is useful for low-dimensional systems but we will not study it in this class.
Idea #2: Function Approximation
Unclear how to do Bayes’ filter updates and predictions in this case.
Idea #3: Weighted Particles
Advantages: easy to predict/update by treating each particle as a separate hypothesis whose weight is updated.
Disadvantages: need enough particles to “cover” the distribution
Higher density of
particles means
higher probability
mass
Want particles to be drawn from the belief at time t:

## Slide 18: Particle Filter Algorithm
Let’s just get an intuition for the whole process now, and we’ll justify why this is right on the coming slides….

## Slide 19: Particle Filter Algorithm
Intuition: use the M particles to “correctly” approx. bel(x)

## Slide 20: Particle propagation/prediction
Simulate what is going to happen to the particle
at the next time step by drawing a sample from
the next state specified in the dynamics (a.k.a.
one-step simulator)
Usually

## Slide 21: Particle Update

## Slide 22: How to update particle weights after an observation
Real state of robot
Measurement model
with and

## Slide 23: How to update particle weights after an observation
Real state of robot
Actual measurement received:

## Slide 24: How to update particle weights after an observation
mth particle hypothesis
Measurement model
with and

## Slide 25: How to update particle weights after an observation
mth particle hypothesis
Q: What is the probability of the actual measurement given the state hypothesized by the particle?
A:

## Slide 26: How to update particle weights after an observation
mth particle hypothesis
Q: What is the probability of the actual measurement given the state hypothesized by the particle?
A:
Assuming range measurements are
conditionally independent given state

## Slide 27: How to update particle weights after an observation
mth particle hypothesis
Q: What is the probability of the actual measurement given the state hypothesized by the particle?
A:
In the figure above this probability would be low
and this particle would be unlikely.

## Slide 28: How to update particle weights after an observation
mth particle hypothesis
Particle’s (unnormalized) weight
See Appendix 1 for why
this choice was made
for the weight

## Slide 29: The distribution of the particles has not been updated yet. We only updated their weights. To update the distribution of particles we need to do resampling

## Slide 30: The distribution of the particles has not been updated yet. We only updated their weights. To update the distribution of particles we need to do resampling
Sample particles with repetition/replacement,
according to their updated weights.

## Slide 31: Resampling Particles
Main goal: Get rid of unlikely particles (with too low weights) and focus on most likely particles (a.k.a. survival of the fittest).
Main mechanism: Sample new set of particles from existing set, with replacement (repetition), so that same particle can be sampled more than once.
Sample old particle i with probability
Many possible ways to implement it. Here we present two algorithms.

## Slide 32: Resampling Particles: Algorithm #1
new_particles = []
sample u ~ Uniform[0,1]
idx = int( u * (N-1) )
beta = 0
max_w = max(weights)
for each of the N particles:
sample v ~ Uniform[0,1]
beta += v * 2* max_w
while beta > weights[idx]:
beta -= weights[idx]
idx = (idx + 1) % N
p = particles[idx].copy()
new_particles.append(p)

## Slide 33: Resampling Particles: Algorithm #2
new_particles = []
sample r ~ Uniform[0, 1/N]
c = weights[0]
idx = 0
for n = 1…N:
u = r + (n-1)/N
while u > c:
idx = idx + 1
c = c + weights[idx]
p = particles[idx].copy()
new_particles.append(p)
w2
w3
w1
wn
Wn-1
Stochastic universal sampling
Systematic resampling
Linear time complexity

## Slide 34: Resampling Particles: Example
Suppose we only have 5 particles:
Particle index | Normalized weight
1 | 0.1
2 | 0.2
3 | 0.4
4 | 0.1
5 | 0.2
Q: What is the probability that after a round of resampling
the highest probability particle (#3) is not sampled?
A:
i.e. there is nonzero probability that we will lose the
highest-probability particle  it will happen eventually

## Slide 35: Resampling Particles: Example
Suppose we only have 5 particles:
Particle index | Normalized weight
1 | 0.1
2 | 0.2
3 | 0.4
4 | 0.1
5 | 0.2
Q: What is the probability that after a round of resampling
the highest-probability particle (#3) is not sampled?
A:
Q: What is the probability that after a round of resampling
one of the lowest-probability particles (#1) is not sampled?
A:

## Slide 36: Resampling Particles: Consequences
Weak particles very likely do not survive.
Variance among the set of particles decreases, due to mostly sampling strong particles (i.e. loss of particle diversity).
Loss of particle diversity implies increased variance of the approximation error between the particles and the true distribution.
Particle deprivation: there are no particles in the vicinity of the correct state

## Slide 37: How to address particle deprivation
Idea #1: don’t resample when only a few particles contribute
Idea #2: inject random particles during resampling
Idea #3: increase the number of particles (may be impractical depending on the computational complexity of the system)

## Slide 38: How to address particle deprivation
Idea #1: don’t resample when only a few particles contribute
  Effective sample size:
  When all particles have equal, normalized weights (1/N) then
  When a single particle carries the entire weight then
  and we have loss of particle diversity.
  Resample only when
Idea #2: inject random particles during resampling
Idea #3: increase the number of particles (may be impractical depending on the computational complexity of the system)

## Slide 39: How to address particle deprivation
Idea #1: don’t resample when only a few particles contribute
Idea #2: inject random particles during resampling
  A small percentage of the particles’ states should be set randomly
    Pro: simple to code, reduces (but does not fix) particle deprivation
    Con: incorrect posterior estimation even when there are infinitely many particles
Idea #3: increase the number of particles (may be impractical depending on the computational complexity of the system)

## Slide 40: Particle Filter Algorithm
Actual observation and control received

## Slide 41: Particle Filter Algorithm
Particle propagation/prediction:
noise needs to be added in order to make
particles differentiate from each other.
If propagation is deterministic then particles
are going to collapse to a single particle after a
few resampling steps.

## Slide 42: Particle Filter Algorithm
Weight computation as measurement likelihood.
For each particle we compute the probability of the
actual observation given the state is at that particle.

## Slide 43: Particle Filter Algorithm
Resampling step
Note: particle deprivation heuristics are not
shown here

## Slide 44: Particle Filter Algorithm
Note: here we work with a fixed number of particles
but in many applications, such as localization, you could work
with a reduced number of particles after the particles have
converged to the true estimate.
Such implementations of particle filters are called adaptive. An
example is the KLD-sampling adaptive particle filter, which is
not going to be covered here.

## Slide 45: Examples: 1D Localization

## Slide 46: Examples: 1D Localization

## Slide 47: Examples: Monte Carlo Localization

## Slide 48: Examples: Monte Carlo Localization
After incorporating 10 ultrasound scans

## Slide 49: Examples: Monte Carlo Localization
After incorporating 65 ultrasound scans

## Slide 50: Using Ceiling Maps for Localization
Image of ceiling

## Slide 51: Vision-based Localization
P(z|x)
h(x)
z

## Slide 52: Under a Light
Measurement z:
P(z|x):

## Slide 53: Next to a Light
Measurement z:
P(z|x):

## Slide 54: Elsewhere
Measurement z:
P(z|x):

## Slide 55: Global Localization Using Vision

## Slide 56: Appendix 1
Why did we choose as the importance weight for particle m?
Main trick: importance sampling, i.e. how to estimate properties/statistics of one distribution (f) given samples from another distribution (g)
For example, suppose we want to estimate
the expected value of f given only samples from g.

## Slide 57: Appendix 1
Why did we choose as the importance weight for particle m?
Main trick: importance sampling, i.e. how to estimate properties/statistics of one distribution (f) given samples from another distribution (g)
For example, suppose we want to estimate
the expected value of f given only samples from g.

## Slide 58: Appendix 1
Why did we choose as the importance weight for particle m?
Main trick: importance sampling, i.e. how to estimate properties/statistics of one distribution (f) given samples from another distribution (g)
For example, suppose we want to estimate
the expected value of f given only samples from g.
Weights describe the mismatch
between the two distributions,
i.e. how to reweigh samples to
obtain statistics of f from
samples of g

## Slide 59: Appendix 1
Why did we choose as the importance weight for particle m?
Main trick: importance sampling, i.e. how to estimate properties/statistics of one distribution (f) given samples from another distribution (g)
For example, suppose we want to estimate
the expected value of f given only samples from g.
Weights describe the mismatch
between the two distributions,
i.e. how to reweigh samples to
obtain statistics of f from
samples of g
In the case of particle filters
Posterior belief after update
Belief after propagation, before update

## Slide 60: Appendix 1
Why did we choose as the importance weight for particle m?
Main trick: importance sampling, i.e. how to estimate properties/statistics of one distribution (f) given samples from another distribution (g)
In the case of particle filters
Posterior belief after update
Belief after propagation, before update