## Slide 1: COMP417 Introduction to Robotics and Intelligent Systems Lecture 17: Extended Kalman Filter
Adapted from an earlier version by Florian Shkurti @ U of T

## Slide 2: Beyond the KF Assumptions
We used the linear forms of motion and measurement (e.g., z=Hx+noise) at several stages to make the equations easier
But, this was not a good thing in general. Real robots almost all have nonlinear motions and measurements!
  E.g., the robots below sense the distance and angle to the landmarks (l) at the edge of the field
  To form this equation, need trigonometry
  and square root of squares
  These are not linear, so are we stuck?

## Slide 3: Plan for today
Happily, we are not stuck!
Let’s extend the KF ideas to nonlinear models:
  First look at what goes wrong exactly
  Then the math to fix it
We’ll end with an algorithm called the Extended Kalman filter, which is the one that is actually used everywhere
  Main math ideas come from KF, but extended to practical robots

## Slide 4: Recommended reading
Chapter 3.3 in Probabilistic Robotics for EKF
Chapter 7.4 in Probabilistic Robotics for EKF-Localization
Chapter 10.2 in Probabilistic Robotics for EKF-SLAM

## Slide 5: Kalman Filter: an instance of Bayes’ Filter
Linear dynamics with Gaussian noise
Linear observations with Gaussian noise
Initial belief is Gaussian
Assumptions guarantee that if the prior belief before the prediction
step is Gaussian
and the posterior belief
(after the update step)
will be Gaussian.
then the prior belief after the
prediction step will be Gaussian

## Slide 6: Kalman Filter: an instance of Bayes’ Filter
Linear dynamics with Gaussian noise
Linear observations with Gaussian noise
Initial belief is Gaussian
Assumptions guarantee that if the prior belief before the prediction
step is Gaussian
and the posterior belief
(after the update step)
will be Gaussian.
then the prior belief after the
prediction step will be Gaussian
Suppose you replace
the linear models with
nonlinear models.
Does the posterior remain
Gaussian?

## Slide 7: Kalman Filter: an instance of Bayes’ Filter
Linear dynamics with Gaussian noise
Linear observations with Gaussian noise
Initial belief is Gaussian
Assumptions guarantee that if the prior belief before the prediction
step is Gaussian
and the posterior belief
(after the update step)
will be Gaussian.
then the prior belief after the
prediction step will be Gaussian
Suppose you replace
the linear models with
nonlinear models.
Does the posterior remain
Gaussian? NO

## Slide 8: Linearity Assumption Revisited
If
and
then

## Slide 9: Nonlinear Function
If
and
then y is not necessarily
distributed as a Gaussian.

## Slide 10: Nonlinear Function
If
and
then y is not necessarily
distributed as a Gaussian.
How can we approximate p(y) using a single Gaussian, without having a formula for p(y)?
IDEA #1: MONTE CARLO SAMPLING
Draw many (e.g. 10^6) samples xi ~ p(x)
Pass them through the nonlinear function yi = g(xi)
Compute the empirical mean (m) and covariance (S) of the samples yi
Return Normal(m, S)
IDEA #2: LINEARIZE THE NONLINEAR FUNCTIONS f, h
- Then we are in the case y = Gx +c, so p(y) is a Gaussian

## Slide 11: Nonlinear Function
If
and
then y is not necessarily
distributed as a Gaussian.
How can we approximate p(y) using a single Gaussian, without having a formula for p(y)?
IDEA #1: MONTE CARLO SAMPLING
Draw many (e.g. 10^6) samples xi ~ p(x)
Pass them through the nonlinear function yi = g(xi)
Compute the empirical mean (m) and covariance (S) of the samples yi
Return Normal(m, S)
IDEA #2: LINEARIZE THE NONLINEAR FUNCTIONS f, h
- Then we are in the case y = Gx +c, so p(y) is a Gaussian
This is how we computed
the Gaussian approximation
of p(y).

## Slide 12: Nonlinear Function
If
and
then y is not necessarily
distributed as a Gaussian.
How can we approximate p(y) using a single Gaussian, without having a formula for p(y)?
IDEA #1: MONTE CARLO SAMPLING
Draw many (e.g. 10^6) samples xi ~ p(x)
Pass them through the nonlinear function yi = g(xi)
Compute the empirical mean (m) and covariance (S) of the samples yi
Return Normal(m, S)
IDEA #2: LINEARIZE THE NONLINEAR FUNCTIONS f, h
- Then we are in the case y = Gx +c, so p(y) is a Gaussian
Bad idea to use in Kalman Filter
because we want to approximate
p(y) efficiently.

## Slide 13: Linearization
Notice how the Linearization
approximation differs from the
Monte Carlo approximation (which
is better, provided sufficiently many
samples).
That said, the Linearization approximation
can be computed efficiently, and can be integrated into the Kalman
Filter estimator  Extended Kalman Filter

## Slide 14: Linearization with low approximation error
The quality of the linearization
approximation depends on the uncertainty
of p(x) but also on the shape of the nonlinearity g(x).
In this example p(x) has small variance so most points will be concentrated around 0.5 and will pass through a very small region of g(x), where g(x) is close to linear.
In this case p(y) is nearly Gaussian,
and the Linearization approximation
matches the Monte Carlo approximation.

## Slide 15: Linearization with high approximation error
The quality of the linearization
approximation depends on the uncertainty
of p(x) but also on the shape of the nonlinearity g(x).
In this example p(x) has high variance so points g(x) will be spread out around g(0.5), where g(x) is not close to linear.
In this case p(y) is multimodal,
and the Linearization approximation
matches the Monte Carlo approximation are both suboptimal approximations. Again Monte Carlo is better, provided sufficient samples.

## Slide 16: How do we linearize?
Using the first order Taylor expansion around the mean of the previous update step’s state estimate:
Constant term
with respect to
the state
Recall how to compute the Jacobian
matrix. For example, if
then the Jacobian of f with respect to
at is

## Slide 17: How do we linearize?
Using the first-order Taylor expansion around the mean of the previous prediction step’s state estimate:
Constant term
with respect to
the state
Recall how to compute the Jacobian
matrix. For example, if
then the Jacobian of f with respect to
at is

## Slide 18: Extended Kalman Filter: an instance of Bayes’ Filter
Linear dynamics with Gaussian noise
Linear observations with Gaussian noise
Initial belief is Gaussian
Assumptions guarantee that if the prior belief before the prediction
step is Gaussian
and the posterior belief
(after the update step)
will be Gaussian.
then the prior belief after the
prediction step will be Gaussian

## Slide 19: EKF in N dimensions
Prediction Step
Update Step
Received measurement but expected to receive
Prediction residual is a Gaussian random variable
where the covariance of the residual is
Kalman Gain (optimal correction factor):
Dynamics
Measurements
Init

## Slide 20: EKF Summary
Efficient: Polynomial in measurement dimensionality k and state dimensionality n: O(k2.376 + n2)
Not optimal (unlike the Kalman Filter for linear systems)
Can diverge if nonlinearities are large
Works surprisingly well even when all assumptions are violated
As in KF, inverting
the covariance of the
residual is O(k^2.376)

## Slide 21: Example #1: EKF-Localization
Given
  Map of the environment.
  Sequence of sensor measurements.
Wanted
  Estimate of the robot’s position.
Problem classes
  Position tracking
  Global localization
  Kidnapped robot problem (recovery)
“Using sensory information to locate the robot in its environment is the most fundamental problem to providing a mobile robot with autonomous capabilities.” [Cox ’91]

## Slide 22: Landmark-based Localization
Landmarks, whose
position
in the world is known.
Each robot measures
its range and bearing
from each landmark
to localize itself.
State of a robot:

## Slide 23: Landmark-based Localization
Measurement at time t,
is a variable-sized
vector, depending on the
landmarks that are
visible at time t.
Each measurement is
a 2D vector, containing
range and bearing from
the robot to a landmark.

## Slide 24: Estimation Sequence (1)

## Slide 25: Estimation Sequence (2)

## Slide 26: Comparison to true trajectory

## Slide 27: Example #2: EKF-SLAM
Given:
  The robot’s controls
  Observations of nearby features
Estimate:
  Map of features
  Path of the robot
A robot is exploring an unknown, static environment.

## Slide 28: Structure of Landmark-based SLAM

## Slide 29: Why is SLAM a hard problem?
SLAM: robot path and map are both unknown
Robot path error correlates errors in the map

## Slide 30: Why is SLAM a hard problem?
In the real world, the mapping between observations and landmarks is unknown
Picking wrong data associations can have catastrophic consequences
Pose error correlates data associations
Robot pose
uncertainty

## Slide 31: EKF-SLAM
Map with N landmarks: (3+2N)-dimensional Gaussian
Can handle hundreds of dimensions

## Slide 32: Appendix

## Slide 33: EKF-SLAM
Map Covariance matrix

## Slide 34: EKF-SLAM
Map Covariance matrix

## Slide 35: EKF-SLAM
Map Covariance matrix

## Slide 36: Properties of EKF-SLAM (Linear Case)
Theorem:
The determinant of any sub-matrix of the map covariance matrix decreases monotonically as successive observations are made.
Theorem:
In the limit the landmark estimates become fully correlated
[Dissanayake et al., 2001]